## Slide 1
jjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjj
Bruno De Troch
Alberto Bellato
Operations efficiency across IP and optical layers

## Slide 2
Agenda
IP/Optical convergence history
IP Routing versus Optical Transport
Coherent pluggables
Platform choices
Management and Operations
Business Aspects
Putting it all together

## Slide 3
The promise of IP-Optical network
convergence
Simplify networks
Reduce equipment
Save space
Reduce power
Drive down cost
The benefits are compelling and so the journey began…
© 2023 Nokia
3

## Slide 4
Management Plane
Control Plane
Data Plane
2000 2020 2025
IP-optical convergence
Over a decade in the making
Router line cards w/integrated transponder
Packet-optical platforms
© 2023 Nokia
4
Are we there yet?
G-MPLS, GMPLS-UNI, ASON…
Converged IP+O management
‘SDN’
Cross-domain management & control
SFF pluggable DCOs in routers

## Slide 5
Agenda
IP/Optical convergence history
IP Routing versus Optical Transport
Coherent pluggables
Platform choices
Management and Operations
Business Aspects
Putting it all together

## Slide 6
7750 SR-14s
12 cards per 24RU
IP Routing
Scale node capacity
Maximize port density
QSFP-DD 800G
36 ports per card
IP Routing versus Optical Transport
Different goals, different focus, different solutions
Optical Transport
Scale link capacity
Maximize fiber throughput/reach
PSE-6s
800G over 2000+ km
Approaching Shannon’s limit

## Slide 7
Silicon
integration
7.2T HD in 22RU
360x 10G SFP+
36x 100G CFP2
FP3
40nm
System
integration
(2012)
FP5
7 nm
172.8T HD in 16RU
1152x 100G QSFP-DD
288x 400G QSFP-DD
144x 800G QSFP-DD
3x capacity
-75% power
(2022)
Capacity and
port density
FP4
16 nm
57.6Tb HD in 16RU
2160x 10G QSFP28
720x 100G QSFP-DD
144x 400G QSFP-DD
(2018)
8x capacity
27x density
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 25 | 75
Power
per bit
400G SR
~25 mW
per Gbps
~100 mW
per Gbps
Evolution of router capacity and resource footprint
Moore’s Law of increasing routing silicon and system integration
What about the pluggables?

## Slide 8
800GAUI
112G SerDes signaling
NPU
Fabric IO
25–30W per cage
PCB
air flow
air flow
heat sink
112G SerDes
Line
card
SFM
SFM
SFM
SFM
Routing silicon
800G transceivers
800GE (coherent) line cards
Unimpeded airflow from front to back
800GE Routing: Technology enablers
Switch fabric
112Gbps SerDes
100G wavelengths
800GAUI
QSFP-DD
formfactor
800G QSFP-DD
pluggables

## Slide 9
Evolution of Coherent Optics
Capacity, Power, Reach
Total network power consumption
normalized Watts per Gb/s
Chart: 
| Gen 1 | Gen 2 | Gen 3 | Gen 4 | Gen 5 | Gen 6
Series 1 | 1 | 0.482 | 0.288 | 0.168 | 0.10533 | 0.0635
94%
reduction six generations
up to 40% less
than prior generation
500 1000 1500 2000
Reach (km)
3x reach
Doubling of optics, space, and power
400G wavelength #1
400G wavelength #2
Gen 6
Gen 5
500 1000 1500 2000
Reach (km)
Costly regens
800G
800G
800G
800G
PSE-6s at 800G/wave
PSE-6s at 800G/wave
Chart: 
| 7nm 95-105Gb | 5nm 130Gb
Column1 | 1
Column2 | 0.47
up to 53% savings
Number coherent interfaces
Normalized to equivalent network capacity
Super-
Coherent
PSE-6
130Gbaud/1.2T
800G Longhaul
100G
PSE
First single-l
100G
33Gbaud/100G
Longhaul
33Gbaud/200G
Metro
SD-FEC
45Gbaud/250G
200G Longhaul
67Gbaud/600G
400G Regional
90Gbaud
400G Anywhere
PSE-2
PSE-3
PSE-V
First
2-ch 500G
First shaped
PCS
Continuous baud rate

## Slide 10
Evolution of Coherent Optics
Modulation format evolution / Data converters / Technology challenges
QPSK
16QAM
PCS
More complex modulation
Higher bitrate
Prob. Const Shaping (PCS)
Improved perf
Transmitter/Receiver
[E/O comp + CMOS(DAC+DSP)]
10011
DAC
Analog
Digital
ADC
Digital
Analog
Sampling rate
Equivalent bandwidth
DAC
DAC
DAC
DAC
DSP
160GBd
200GSps
140GBd
180GSps
95GBd
120GSps
Lower CMOS geometry
higher sampling rate
Enable higher Baudrate
Larger bandwidth
Spectral efficiency is plateauing: Focus on higher Baudrate to increase reach (constant client) and power reduction
Need to choose the appropriately CMOS node for a given Baudrate
… otherwise, performance is limited

## Slide 11
Enabling Coherent Photonic Service Engines
A Fully Vertically-Integrated Approach
Multi-Chip Module Integrated opto-electronic co-design and packaging optimized for performance
Coherent modem algorithms
Probabilistic
Constellation Shaping
Advanced
Analytics
Continuously Tunable Baud Rate
CMOS manufacturing
High-performance optics
Advanced flip-chip BGA packaging
Silicon photonics
5nm DSP
130Gbaud 1.2Tb/s
130GBaud optics
CDM and ICR
Client
Optics
Line
Optics

## Slide 12
IP-Optical view of applications
Know the destination
Access and metro DCI
Point-to-point
traffic and fiber
Metro/regional aggregation
Hub and spoke traffic
over fiber rings (typically)
Long haul and subsea
Mesh traffic over long spans and multi-degree nodes
Increasing reach & complexity
Drives IP-O technology & solution requirements
Metro/regional edge/core
Mesh traffic over interconnected fiber links
© 2023 Nokia
12

## Slide 13
Agenda
IP/Optical convergence history
IP Routing versus Optical Transport
Coherent pluggables
Platform choices
Management and Operations
Business Aspects
Putting it all together

## Slide 14
Technology: coherent optics
Full speed ahead!
The challenges:
Capacity
Form factor
Reach
Power
Interoperability
© 2023 Nokia
14
Sweet spot: 400G Access, metro DCI & metro/regional applications
400G QSFP-DD ZR/ZR+ (-10dBm)
400G QSFP-DD ZR+ (0dBm)
800G QSFP-DD ZR/ZR+
25km unamplified
120km with pluggable OLS
450km with ILA
80km unamplified
120km with pluggable OLS
650km with ILA
Est 27-30W
10km unamplified
120km with ILA
SFF pluggable coherent optics go mainstream
Available now
Emerging
2H24

## Slide 15
Long-haul 800GE transport
800G transport over long-haul distances (2000km+)
3x the reach of 7nm/90-100Gbaud solutions
Single-wavelength 800GE long-haul transport without regens
Flexible and efficient multi-service transport
Support wide range and mix of clients
Up to 24x100GE/OTU4, 6x400GE or 3x800GE
Efficient and flexible transport from metro to long-haul
Maximize scale and performance from metro to long-haul
Flexible support for wide range of clients and wavelength speeds
Maximize 800GE bandwidth efficiency
Single 2.4Tb/s linecard supports up to 3 x 800GE
3x the capacity/linecard of current 800G solutions
Metro, DCI and IX interconnection

## Slide 16
Agenda
IP/Optical convergence history
IP Routing versus Optical Transport
Coherent pluggables
Platform choices
Management and Operations
Business Aspects
Putting it all together

## Slide 17
Technology: platforms & integration
Some curves to navigate
Coherent optics support
Power & cooling
Optics integration
Routers / Transponders
Requirements for both optical platforms & routers
© 2023 Nokia
17
In-line amplification
Fiber/DWDM mux
(Open) ROADMs
Line Systems

## Slide 18
Hop-by-hop routing versus reconfigurable add-drop multiplexors
Forwarding IP transit traffic at the most economical layer
60W
36W
4W
Optical line system
(FOADM or ROADM)
Total Power: 100 Watts/400GE
400G IP transit hop
High
Low
Cost/bit
Power/bit
Latency
IP fabric
(Layers 1-3)
Electrical-Optical
(400ZR+ DCO)
4W
96% less power by forwarding IP traffic at the optical layer
400G IP express

## Slide 19
Agenda
IP/Optical convergence history
IP Routing versus Optical Transport
Coherent pluggables
Platform choices
Management and Operations
Business Aspects
Putting it all together

## Slide 20
Technology: management & operations
An uphill climb
Link up/down
Access (400ZR)
Channel plan
Power ramp
Link up/down
Metro DCI (P2P 400ZR)
Active power management
Modulation
Channel plan
Power ramp
Link up/down
Metro DCI (P2P 400ZR+)
Path compute
Optical add/drop
Dynamic gain equalization
Active power management
Modulation
Channel plan
Power ramp
Link up/down
Metro/regional (ROADMs)
Optical add/drop
Dynamic gain equalization
Active power management
Modulation
Channel plan
Power ramp
Link up/down
Metro/Regional Agg’n (2D ROADMs)
IP team
IP-optical coordination
Optical team
IP-optical co-ordination required
Reach and complexity
© 2023 Nokia
20

## Slide 21
IP-Optical Management Architecture
End-End coordinated cross-domain management
400G ZR+
ROADM-enabled
Optical Line System
400G ZR+
400G
Multihaul
400G
Multihaul
Optical team
IP
team
IP management
T-API
IP Layer
IP Layer
Optical Layer
WaveSuite
Network Operation Center
Optical M&C
Resource
Controller
Open
Terminal
Control
Edge
Port
Discovery
Planner
IP + Optical Fault Management
Intent Based Prov.
Cross Domain Coordinator
T-API

## Slide 22
Agenda
IP/Optical convergence history
IP Routing versus Optical Transport
Coherent pluggables
Platform choices
Management and Operations
Business Aspects
Putting it all together

## Slide 23
Business aspects
Before even starting the trip
© 2023 Nokia
23
Are the business objectives well understood?
Is the business case for the project compelling?
Commercial objectives
Organization
Are IP and optical transport teams under common management?
Which team takes the project lead?

## Slide 24
Agenda
IP/Optical convergence history
IP Routing versus Optical Transport
Coherent pluggables
Platform choices
Management and Operations
Business Aspects
Putting it all together

## Slide 25
IP-Optical convergence
Putting it all together
3 keys to success
Business
Organization
Commercial objectives
Applications
Technology
Pluggable DCOs
Platforms
Management & operations
P2P access/ metro DCI
Metro/regional aggregation
Metro/regional edge/core
Long haul / subsea
© 2023 Nokia
25

## Slide 26
© 2023 Nokia
26
Are we there yet?
Lots of progress, but still a lot of road ahead!