## Slide 1
Gloria Vuagnin - GARR
Lessons Learned
Deploying a Pilot Spectrum Connection Service over GARR/GÉANT
TNC23 – Lightning talk
Tirana, June 7th 2023

## Slide 2: Ultra-high capacity connection
1.6 Tbp/s
High Energy Physics Tier0
HEP
Italian
Tier1
‘‘LHC requirements for Run4 (2029) […] Larger Tier1s are supposed to get connected to CERN and to their Tier2s at 1 Tbps.’’
Martelli Edoardo, “Networks for High Energy Physics: LHCOPN and LHCONE”, AmRP Working Group Meeting (11 Oct 2022)

## Slide 3: Spectrum connection service (SCS) WP7-T2 of GN4-3
SCS Users (huge capacity consumers) own the coherent transponder or transceiver
SCS Providers own and operate their Open Line System giving access to an empty slice (e.g 100-400GHz) of their available spectrum (the extended C-band has 4.8THz of spectrum)
User-to-Network Interface (SCS-UNI) defines the boundaries between users and providers (e.g. a LC port on a patch panel).
Network-to-Network Interface (UNI-NNI) defines the demarcation point between providers (e.g. a patch cord between ROADMs).
Traditional C-Band
Spectrum THz
Extended
C-Band
191.3
192.1
196.1

## Slide 4: CERN-CNAF/INFN datacenter interconnection
~ 1000 km
Demarcation Point between GÉANT and GARR in Milan PoP
Pilot of the Spectrum Connection Service (SCS)
GARR and GÉANT optical network have a partially disaggregated architecture
Co-located PoP in Milan
Use of DCI/Transponders boxes @ end-points
Pure optical connection that uses an empty slice of the optical spectrum available on GÉANT and GARR fibre infrastructure

## Slide 5: The multi-domain open line system
GARR OLS
GÉANT OLS
Add/Drop
ROADM
3 x AMP
Add/Drop
ROADM
8 x AMP
GÉANT and GARR PoPs in Milan are 10m apart
Geneva
PoP
Bologna
PoP
GÉANT-GARR NNI
Infinera FlexILS
Route&Select ROADM: Pravicy and spectrum policing and shilding

## Slide 6: User-Network Interfaces
CERN – GÉANT UNI
in Geneva
Privacy is guarantee by a dedicated power splitter/combiner add/drop card in Geneva,
by a add/drop optical switch card in Bologna
CNAF – GARR UNI
in Bologna
1.6Tbps on 4 carriers each of them:
DP-16QAM- 400Gbps
100GHz
27% SD FEC
69Gbaud
Infinera G30 - CHM2T
100-600Gbps wavelength
4x100/1x400 GbE clients

## Slide 7: Telemetry data from G30 through gRPC

## Slide 8
gloria.vuagnin@garr.it
Any questions? Please, send me an e-mail
Thank you
The SCS pilot is successfully showing its great potential. Be tuned to the upcoming GÉANT SCS service launch