## Slide 1
David Franco
Asier Atutxa
A production-ready UPF based on RARE
Towards affordable high-performance 5G networks
Rennes, France
12 June 2024

## Slide 2: Content
5G
RARE router
UPF implementation
Scenario under consideration
Conclusions

## Slide 3: 5G: vision
Mobile broadband is the fundamental technology for interconnecting communities and individuals
5G will continue growing with more that 4.4 billion subscribers predicted by 2027*
The impact of mMTC
Notes: *Forecast
Source: Ericsson (2022), statista
5G mobile subscriptions worldwide

## Slide 4: 5G: vision
Five tier one vendors
High CAPEX/OPEX
The market share is growing for "Other" vendors
Open-source solutions
Startups
More customizable and affordable products

## Slide 5: 5G: architecture
Radio Access Network
Base station (gNB)
Function split (DU-CU)
Fronthaul/Midhaul links
Standard 5G RAN deployment

## Slide 6: 5G: architecture
5G core
Service Based Architecture (SBA) framework
A set of interconnected Network Functions (NFs) to provide:
  the control plane functionality
  common data repositories
NFs
  Self-contained, independent and reusable
  Expose services through well-defined interfaces: REST, QUIC
Standard 5G Core deployment

## Slide 7: 5G: deployment
Example of 5G deployments
5G containerization
  NFs at different locations
  Not all the configurations are possible

## Slide 8: 5G: deployment
Example of 5G deployments
5G slicing
  Duplication of NFs
  Each slice for a type of traffic (URLLCc, eMBB, mMTC)

## Slide 9: RARE router
Router for Academia, Research & Education (RARE)
Production ready routing and switching functionalities
GEANT 5th programme
Control and data plane separation
  Control plane: freertr
  Data plane: rare
    Programmable data plane
    P4, DPDK, XDP, libpcap

## Slide 10: RARE router
Functionality
Routing & forwarding
  IP, LLDP, VLAN, MPLS, BGP, OSPF, BFD
Tunneling
  GRE, L2TP, VXLAN, GTPv1, IPsec, MACsec, wireguard, openvpn
Management
  Telnet, SSH
Performance
Tested at 100 Gbps (Tofino ASIC)
Tested at 400 Gbps (Tofino2 ASIC)

## Slide 11: UPF implementation in RARE
Target
  Provide a standalone UPF
Motivation
  Affordable UPF solution
  Enhance the performance between the RAN and the Data Network (DN)
    More users
    Higher data rate
    Lower delay/jitter

## Slide 12: UPF implementation in RARE
Implementation
N5 interface: PFCP protocol (tested)
N3 interface: GTPv2 protocol (ongoing)
N6 interface: IP protocol (already available)

## Slide 13: Scenario under consideration
Smart Networks for Everything (SmartNets4E1)
An infrastructure for network research
Three nodes interconnected at 100G
Research resources for 5G/6G in different verticals
  Advanced manufacturing (CFAA node)
  Health, education, transportation and mobility (BILBAO node)
Integrated into the ESFRI SLICES-RI
Collocated with GEANT’s PoP (LEIOA node)
1 https://i2t.ehu.eus/en/resources/smartnets4e

## Slide 14: Scenario under consideration
SmartNets4E: BILBAO location
Computing nodes
Commercial and experimental 5G NPN
Quantum Key Distribution (QKD) equipment
  Secure communication between CFAA and BILBAO
Network analysis and testing equipment:
  Traffic generator
  Impairment generator
Experimental P4 network

## Slide 15: Scenario under consideration
SmartNets4E: CFAA location
Advanced manufacturing R&D
Indoor commercial 5G NPN (mmWave)
Experimental 5G NPN
  LTE-M and NB-IoT support
IIoT sensor network
Quantum Key Distribution (QKD) equipment
  Secure communication between CFAA and BILBAO

## Slide 16: Scenario under consideration
SmartNets4E: LEIOA location
Interconnection site
  GEANT PoP
  RedIRIS PoP
Computing nodes
Outdoor commercial 5G NPN
  Campus network

## Slide 17: Use case
The role of RARE-UPF
The scenario in our research infrastructure

## Slide 18: Use case
Video:
SmartNets4E : the 3 locations of the experimentation facility
5G and RARE infrastructure
PFCP implementation in RARE

## Slide 19: Conclusions and next steps
Conclusions
High-performance user plane for 5G core network
Multi-UPF scenario
Next steps
Performance tests
Implementation of other 5G entities: SMF, N3IWF, etc.
Remote access and management tools

## Slide 20
david.franco@ehu.eus
asier.atutxa@ehu.eus
Any questions?
Thank you