## Slide 1
Sebastiano Buscaglione & Olaf Verschoor
Internet’s backbone
How to build an Internet sub-marine cable?
Brighton - TNC25
Tuesday June 10 2025

## Slide 2: A 170 years old business….
The first Intercontinental Communication Cable was laid in 1858…
…it failed shortly, but successive attempts in 1865/66 produced the first successful cable.

## Slide 3: …is it still relevant? Subsea cables, do we really need them?
“Are satellites not the future?”
Feature | 🌊 Submarine Cables | 🛰️ Satellite Internet
Data capacity | Extremely High (Tbps scale) | Lower (Gbps scale)
Latency | Very low / ± 60 ms | High 50 – 500 ms
Reliability | Very stable | Affected by weather / space congestion
Cost per bit | Low | Higher
Use case | Core Internet backbone | Connect underserved / remote locations
Submarine cables account for over 99% of intercontinental data
traffic source: TeleGeography 2023

## Slide 4
source: www.submarinecablemap.com

## Slide 5: Submarine cables are indispensable for research and education.
Bandwith intensive science
Latency sensitive collaboration
Cost per bit
Uptime & Reliability
Security & Sovereignty

## Slide 7: But what do these systems really look like?
Data Centre
Backhaul
Cable Landing Station
Fronthaul
Beach Manhole
Optical Amplifier
Branching Unit

## Slide 8: Data Centre
Final termination of the System – here data can be encoded for transmission using DWDM.

## Slide 9: Toward the CLS – the backhaul
Data Centre
Backhaul
Cable Landing Station
Fronthaul
Beach Manhole
Optical Amplifier
Branching Unit
Backhaul is typically a ring of fibre between the CLS and the Data Centre. Signals are protected optically across this ring.

## Slide 10: The Cable Landing Station (CLS)
Frequently, and purposefully, an unassuming building – main role is to host the Power Feeding Equipment (PFE) for the system.
What Power?
A subsea cable can only be powered from the edges. Here 1000s V DC current is provided to power all active elements, such as Amplifiers and Branching units equipment (WSS).
Sometimes CLS also host terminating equipment.

## Slide 11: Between CLS and Beach Manhole – the fronthaul
Data Centre
Backhaul
Cable Landing Station
Fronthaul
Beach Manhole
Optical Amplifier
Branching Unit
The Fronthaul cable carries power therefore the CLS and Beach Manhole should be as close as possible.

## Slide 12: Beach Manhole (BMH)
It is literally – just a manhole, close to the beach.
It physically terminates the “subsea” portion of the cable system, moving from a hardened cable to a much smaller and flexible one.

## Slide 13: In the water
Data Centre
Backhaul
Cable Landing Station
Fronthaul
Beach Manhole
Optical Amplifier
Branching Unit
Deep
Shallow
Shallow - in reach of human activities, such as Anchors and Fishing Nets. Deep – anything out of reach for that.

## Slide 14: The cable itself
In shallow water and where there is higher risk of Physical damage the cable is “armored” using steel wires.
In deep water armoring is not required as the risk of physical damage is low.
In shallow water, especially close to the costal area, the cable installation is also more complex, frequently requiring burial or other installation strategies to both protect the cable as well as the environment.
Each cable is custom built for a specific project.
Weight and size matters a lot for cost management!

## Slide 15: The cable system – repeaters and branching units
Repeaters are installed every ~80Km to “boost” signal strength.
Branching units might also be present to manage system “branches”.
All these elements are hardened and have high level of redundancy to allow for uninterrupted operation for 20+ years.

## Slide 16: Costs & Financing
Costs determined by many factors
Complexity of cable system
Route / seabed
Investor
Public investors
Governments / EC
Banks / loans
Anchor tenants
Telcos
Others
Chart: 
| Marine installation & ships | Cable equipment manufacturing | Marine survey / route design | Landing stations & backhaul | Permits
 | 0.35 | 0.3 | 0.125 | 0.125 | 0.1

## Slide 17: Building a sub-marine cable system
Time and planning
  Time between initial concept/plan and actual install is several years (5-10)
  Economical lifespan of a cable system is more than 25 years
Initiation
6-12 months
Financing
6-12 months
Route design
6-9 months
Manufacturing
12-18 months
Maribe Survey
12-18 months
Installation
6-9 months
….and in this time a lot can happen

## Slide 18: Building a sub-marine cable system
Limited number of cable manufacturers
SubCom (USA)
Alcatel Submarine Networks (France)
NEC (Japan
HMW (China)
Cable laying ships
Limited capacity
Need to reserve years in advance
In sync
Route & Engineering
Investment
Contracts
Working capital
Permits

## Slide 19
Any questions?
Thank you
sebastiano.buscaglione@geant.org
olaf.verschoor@geant.org