## Slide 1
David Maier
NRENs in transition to a quantum-safe future
SURF's QKD testbed deployment
david.maier@surf.nl

## Slide 2: Intro: Quantum Threat vs NREN
Quantum Threat: widely-used encryption protocols (e.g. RSA, ECC) will be broken within the next decade
Classical threat: members confused about migration to quantum-safe (PQC vs. QKD?)
NRENs uniquely positioned:
  Trusted infrastructure and innovation providers
  At the heart of national research, education, and policy development
  Embrace our role of leading the transition!

## Slide 3: Overview QCINed
QKD
Threat assesment
PQC
Source: https://quantumdelta.nl/qcined
Government use-case
SURF: ISP / NREN use-case
TU/e: industry
use-case
3 different use-cases/ focus areas
Involvement of different stakeholders (NSAs, R&E, industry)
MDI, CV/DV – QKD from different vendors
11km
7km

## Slide 4: QCINed: Challenges
Software (KMS, QKM) either proprietary, bad or both (back then)
Vendors not or barely interoperable
Available domain control models using centralized approach
Range limitation making the N in NREN impractical → QKD-as-a-Service
→ open-source KMS (key relaying, fully vendor agnostic), domain control and orchestration
?
?
QKDaaS

## Slide 5: Overview QCINed @ SURF
QKD-as-a-Service for R&E
Testbed connecting Amsterdam and Utrecht
Embedded in SURF service delivery
Building on our experience in network operation and A&O
Abstraction beyond (vendor-specific) hardware limitations
Open-source solutions
R&E use cases
Amsterdam HPC/ future QC
DC
Utrecht
Trusted Node
UniU
UMC
MDI-QKD
Metropolitan network
DV-QKD
‘Long Reach’ Link
Source: OpenStreetMap
1.8km
11km
7.1km
70.1km

## Slide 6: Open Software Stack
Full open-source software stack
Fully integrated with production A&O workflow orchestrator
eduQDC: quantum domain controller
eduKMS: key management server
QKD
Threat assesment
PQC
Service A&O
WorkflowOrchestrator.org
Domain Control
eduQDC
QKD
Vendor #1
QKD
Vendor #2
KMS
eduKMS
REST API
config
eduQKD repo

## Slide 7: Open Software Stack
eduQDC:
  Minimalist approach
  Only pushes config
eduKMS:
  Fully decentralized
  ETSI 014
  Key-relaying
  Vendor agnostic
  “Continuous key propagation”
QKD
Threat assesment
PQC
Service A&O
WorkflowOrchestrator.org
Domain Control
eduQDC
QKD
Vendor #1
QKD
Vendor #2
KMS
eduKMS
REST API
config
eduQKD repo

## Slide 8: Open Software Stack
If you need a fully open-source software stack to get your organization into QKD: Get in touch!
QKD
Threat assesment
PQC
Service A&O
WorkflowOrchestrator.org
Domain Control
eduQDC
QKD
Vendor #1
QKD
Vendor #2
KMS
eduKMS
REST API
config
eduQKD repo

## Slide 9: QKD use cases
Use case development / exploration crucial for engaging our members
“Classical” QKD use-cases
  MAC-Sec
  IP-Sec
  TLS
  Application-specific encryption
“Beyond” QKD use-cases (possible with current QKD hardware)
  Secure multi-party computation via quantum oblivious transfer (see e.g. “QuGenome: Quantum Enabled Private Recognition of Composite Signals in Genome” in MadQCI)
  QgeKO: Quantum Secure Distribution of Precise Global Navigation Satellite System Keys and Order

## Slide 10: QKD use case PoCs @ SURF
Cloud storage (SURFDrive) using QKD enabled TLS (via openssl)
QKD enabled VPN (wireguard, eduVPN)
Student projects & hackathons (e.g. quantum-safe … : voting app, chat, TLS in RUST; ETSI client for java-script) → Application layer: e.g. QKD as session key or OTP → Transport layer: e.g. QKD as symmetric key (instead of DH) → Network layer: e.g. QKD as symmetric key in ESP in IPSec (periodic cycling) → Data link layer: e.g. QKD as symmetric key in AES-GCM in MACsec
Important: QKD only secures key exchange, not authentication (→ quantum-safe PKI using PQC for authentication)

## Slide 11: Conclusions
NRENs well positioned to lead transition to quantum-safe communication → great use-cases for both QKD and PQC → trusted innovators with “neutrality” between the two solutions
A full open-source software stack is available → encourage collaboration
Use case development and stakeholder engagement is important to lead the transition
Quantum-security of a service needs to be evaluated as a whole (and will likely include PQC and QKD)

## Slide 12
Any questions?
Thank you
david.maier@surf.nl