## Slide 1
Sergejs Kozlovičs, Rihards Balodis, Ināra Opmane
(and a bit of Layer 4)
On Quantum-Secure Layer 3 (IP) and Layer 2 Networking
TNC25 @ Brighton, UK
June 11, 2025
Institute of Mathematics and Computer Science University of Latvia

## Slide 2
IMCS UL Institute of Mathematics and Computer Science of University of Latvia
Founded:
1959
Now:
One of the largest and most influential research institutions in Latvia, EU
Formerly:
The Latvia Computing Center

## Slide 3: IMCS UL: Latvian/Baltic/European Internet
1990-ties:
  IMCS UL connects Latvia to the global Internet
Before 2000-ties:
  IMCS UL actively cooperated with DANTE and NORDUNET, and partnered with the TEN34 (19 countries) and BaltNet projects
Since 2000-ties:
  IMCS UL has been a partner in all GÉANT projects GN1/2/3/4 Latnet/Sigmanet (part of IMCS UL) is a long-term GÉANT partner
  IMCS UL is is a partner now (we maintain a GÉANT node)
August, 1990: first e-mail via a modem connection
October, 1992:
Riga-Tallinn permanent link, 2400 bits/second

## Slide 4: IMCS UL: Quantum Connections
2019, and 2020-ties:
  IMCS UL introduces the very first quantum communication Channels in Latvia
Since 2023:
  Conventional telecommunications industry partners (LVRTC, TET, ECO) turn towards quantum communications
2019:
the first in-lab quantum link
2021:
the first metropolitan-scale link in Riga (33km), with partners

## Slide 5: Towards the Quantum Internet
Stephanie Wehner et al. Quantum internet: A vision for the road ahead. Science 362, eaam9288 (2018)

## Slide 6: Towards the Quantum Internet
The Quantum Internet can wait (entanglement distribution, distributed quantum computing...)
Quantum-secure key exchange cannot wait!

## Slide 7: The Quantum Threat
TLS 1.3 and below
ECC, RSA,
...

## Slide 8: Harvest Now, Decrypt Later
Most quantum-vulnerable algorithms should be:
deprecated by 2030 and
disallowed by 2035.
[NIST Internal Report, NIST IR 8547, “Transition to Post-Quantum Cryptography Standards”]

## Slide 9: Our Motto: Fight Quantum with Quantum!
QRNG
QKD
PQC
considered quantum-safe
(AES: limited speedup by Grover’s search; OTP is information-theoretically secure)
entropy
entropy
quantum hardware
quantum-safe
algorithms
AES, OTP
considered quantum-safe (believed to be hard problems for the quantum computer)

## Slide 10: QRNGs: Quantum Random Number Generators
Quantum Random Number Generators utilize inherently random quantum processes (nuclear decay, photon behaviour, quantum vacuum fluctuations)
Each QKD device must have one.
QRNGs are essential for PQC algorithms:
uniform bitstring sampling
nonces
seeds
salt...

## Slide 11: Our QRNG as a Service
We developed:
QNRG as a Service (qrng.lumii.lv), 2022
  the first QRNG service secured with PQC
Linux kernel module (/dev/qrandom0 simulation)
Windows DLL with Detours (non-open-source)
D-Bus QRNG service
OpenSSL3 provider

## Slide 12: Our Motto: Fight Quantum with Quantum!
QRNG
QKD
PQC
considered quantum-safe
(AES: limited speedup by Grover’s search; OTP is information-theoretically secure)
entropy
entropy
quantum hardware
quantum-safe
algorithms
AES, OTP
considered quantum-safe (believed to be hard problems for the quantum computer)

## Slide 13: QKD vs. PQC
QKD | PQC
Perfect Forward Secrecy | Vulnerabilities can be found in the future Have to withstand the test of time
Information-Theoretically Secure | Not Information-Theoretically Secure
Non-breakable unless Quantum Mechanics are false | Believed to be quantum-safe Breakable with unlimited computational power
Expensive: devices and infrastructure needed | Operates on existing Internet infrastructure
Difficult to configure and maintain | Integrates well into existing software and Public Key Infrastructure (PKI)
No authentication | Provides Authentication and Encryption (AE)

## Slide 14: The Four-Wheel Drive Engine Model (Hybrid!)
QKD
PQC
IDQ
NIST selected
Juniper
Cisco

## Slide 15: GÉANT + QKD: The Problem
Infinera DTN-X optical equipment over dark fibre
Dark fibre is good for quantumness!
But: Optical Transport Network (OTN) switching…
Optical routing/switching is a problem, since we cannot copy an unknown quantum state

## Slide 16: GÉANT + QKD: The IDEA!
QKD as a Service
“WP6 Task 1 is currently reviewing network support requirements for Quantum Technology and quantum key distribution/exchange (QKD/QKE) technology in order to consider its applicability as a service for use by the GÉANT community.”
[NETDEV: https://wiki.geant.org/display/NETDEV/QT]

## Slide 17: Our Solution #1: the Backbone
Replace your cable with our backbone!
We offer a network segment (trunk) secured with quantum keys.

## Slide 18: Our Solution #1: the Backbone
Can be implemented via:
L2 encryptors with QKD support (Centauris)
L3 routers/firewalls with QKD support (Cisco, Juniper)
certified devices!
preferrably, with PQC support

## Slide 19: Our Solution #2: Access via PQC VPN
L2/L3 VPN:
classical
and PQC

## Slide 20: One More Problem, Sorry 
PROBLEM:
distance ~150km
(for most commercial QKD devices)

## Slide 21: Trusted Nodes

## Slide 22: Complex Topologies
Key Relay algorithms are needed
We have to sacrifice some QKD keys for that (a precious resource!)
In the LatQN project, we are implementing the "triangle" topology between different partners in Latvia
=> latqn.eu
(part of EuroQCI)
The research is supported by the European Union, project No. 101091559 ”Development of experimental quantum communication infrastructure in Latvia (LATQN)”.

## Slide 23
EuroQCI = European
QKD "Internet"

## Slide 24
How to provide QKD as a Service for end users without L2/L3 hardware or VPN software?

## Slide 25: Our Solution #3: TLS (Layer 4) Integration
We developed a library (Java and native) that implements TLSv1.3 secured with quantum keys
We replace TLS Key Exchange with an abstract Key Encapsulation Mechanism, KEM (like in PQC)
“Quantum KEM” does not exchange keys but obtains them from quantum devices

## Slide 26: Our Solution #3: TLS (Layer 4) Integration
“Quantum KEM” implementations:
Direct ETSI QKD GS 014
Direct CISCO SKIP
Our original double-secure Butterfly Protocol

## Slide 27: Our Double-Secure Butterfly Protocol
qkd.lumii.lv
QKD as a Service via our
Butterfly Protocol
with
TLSv1.3 integration

## Slide 28: Butterfly Protocol as KEM in TLSv1.3

## Slide 29: Please do not take technology for granted!

## Slide 30: Further Projects
Lat-LitQN:
Riga (LV) - Kaunas (LT) - Vilnius (LT)
with the ability to connect to Poland
Quantum Shield for Data:
Quantum-Secure Access to the Cloud
Quantum-Secure Backups for Data

## Slide 31: Satellite QKD?
Satellites could help establish long-distance QKD without the need for trusted nodes.
Entanglement-based protocols can be utilised (although quantum memory is required in some cases).
We and the satellites:
During 1997-1999, IMCS UL operated an international satellite channel between IMCS UL (LV) and Crawford Communications (US)
During the Lat-LitQN project, we are going to do research on QKD via satellites
Huttner, B., Alléaume, R., Diamanti, E. et al. Long-range QKD without trusted nodes is not possible with current technology. npj Quantum Inf 8, 108 (2022). https://doi.org/10.1038/s41534-022-00613-4

## Slide 32
Any questions?
Thank you
sergejs.kozlovics@lumii.lv
imcs@lumii.lv