## Slide 1: The CERN experiments’ journey towards IPv6-only
Tim Chown (Jisc)
tim.chown@jisc.ac.uk
TNC 2026, Helsinki, 10 Jun 2026
The ATLAS calorimeter © 2005-2024 CERN (License: CC-BY-4.0)
With credit to everyone in the HEPiX
IPv6 WG and those at all the WLCG
sites who made IPv6 happen

## Slide 2: Milestones on the journey to IPv6
Are we there yet?
1995 – IETF RFC1883 – the first core IPv6 standardisation
2004 – Many NRENs deployed IPv6 on their backbones during the 6NET project
2011 – Top-level RIRs declare unused IPv4 address space exhausted
2012 – World IPv6 Launch on June 6
2017 – IETF RFC8200 published as a full Internet Standard
  Good news!
  IPv6 has run on NREN backbones for over 20 years!

## Slide 3: And IPv6 has just become the dominant user IP protocol
https://www.google.com/intl/en/ipv6/statistics.html
That’s 50.4%
worldwide as
of April 2026

## Slide 4: IPv6 is present and enabled in all modern operating systems, devices, routers, etc So, what’s the problem?

## Slide 5: R&E deployment is slow - less than 10%

## Slide 6: But there is one excellent exception to the R&E IPv6 trend!

## Slide 7: WLCG infrastructure
Many experiments: ATLAS, Alice, LHCb, CMS, …
Mission to store, distribute and analyse data
Sites in three tiers:
  Tier-0: CERN, home of the LHC
  Tier-1s: 17 national laboratories
  Tier-2s: 160 university physics departments
Networking:
  LHCOPN (private optical, Tier-0 to Tier-1s)
  LHCONE (L3VPN/VRF, between any Tiers)
  General NREN R&E networks (catchall)

## Slide 8: IPv6 deployment – driven by the HEPiX IPv6 WG
Phase 1: to consider whether and how IPv6 should be deployed in HEP, especially for WLCG
Readiness and gap analysis of software and systems – started in 2011, completed
Phase 2: dual-stack deployment – enabling and preferring IPv6
Dual-stack at data servers – started 2018, now complete
Dual-stack worker nodes – ticket campaign started Dec 2023 – 75% complete, 15% in progress
Phase 3: move towards a single protocol – simpler operation, simpler security, no NAT, Scitags, …
Decommission IPv4 on WANs and migrate to IPv6 only – ongoing

## Slide 9: So where are we now with use of IPv6 for WLCG data transfers? We can see from a variety of sources…

## Slide 10: Traffic on a given OPN link – KIT (DE) – over 99.5% IPv6
Total IPv4 in 24 hours = 17.2Gb in, 4.6Gb out
Total IPv6 in 24 hours = 4.64Tb in, 2.77Tb out

## Slide 11: FTS logs – includes non-WLCG transfers – over 93% IPv6
FTS is the CERN
File Transfer Service
These plots are for
ALL FTS transfers
Most transfers
use a “stack” of
Rucio, FTS and
an underlying tool
such as XRootD

## Slide 12: Scitags plots – flows into RAL(UK) – over 99.9% IPv6
Mean volumes:
IPv6: 5.90GB/s in
IPv4: 2.03MB/s in
Scitags supports the
identification of traffic by
science domain and activity
https://scitags.org/
It includes per-packet
marking for IPv6 traffic
= INNOVATION!

## Slide 13: So, everything’s looking good? Yes, but if we don’t need IPv4 we should now be turning it off wherever we can

## Slide 14: Phase 1: Removing IPv4 on CERN–Tier-1 LHCOPN links
Experiments:
█ = Alice █ = Atlas █ = CMS █ = LHCb
Last update:
- 20260528
- edoardo.martelli@cern.ch
10Gbps
100Gbps
200Gbps
400Gbps
800Gbps
Line speeds:
20Gbps
10Gbps
40Gbps
IPv4
US-FNAL-CMS
AS3152
█
FR-CCIN2P3
AS789
█ █ █ █
ES-PIC
AS43115
█ █ █
DE-KIT
AS58069
█ █ █ █
CH-CERN
AS 513
█ █ █ █
RRC-JINR
AS 2875
█
US-FNAL
AS 3152
█
KR-KISTI
AS 17579
█
CA-TRIUMF
AS 36391
█
FR-CCIN2P3
AS 789
█ █ █ █
NDGF
Scandinavia AS 39590
█ █
DE-KIT
AS 58069
█ █ █ █
ES-PIC
AS 43115
█ █ █
PL-NCBJ
AS 198743
█
CN-IHEP
AS3460
█
US-BNL
AS 43
█
NDGF
CH-LHEP AS 216467
█
RS-SCC-T1
AS
█
RO-UPB
AS2614
█
CH-CERN
AS 513
█ █ █ █
NL-T1
SARA AS 1103-1162
NIKHEF AS 1103-1104
█ █ █
UK-RAL
AS 43475
█ █ █ █
IT-INFN-CNAF
AS 137-2038
█ █ █ █
5 of 17 Tier-1 links now IPv6-only: FNAL, BNL, NCBJ, UPB, PIC

## Slide 15: The IPv6-only schedule
All Tier-1 OPN links due to be IPv6-only by the end of 2026,
making them IPv6-only for the next Data Challenge in Feb 2026
- preparing for the High Luminosity LHC Phase in 2030
All LHCONE links due to be IPv6-only by the end of 2028,
making them ready for the bigger Data Challenge in 2029

## Slide 16: In closing - our key messages to you…
IPv6 is mature in R&E networks
Nearly 100% of the WLCG’s WAN transfers are IPv6
Some WAN links already IPv6-only
Dual-stack is not the end game
If you’re enabling IPv6, also plan where and when you can turn off IPv4
NRENs should encourage and support existing and especially new projects to use IPv6 from day 1

## Slide 17: Thank you! With credit to the HEPiX IPv6 WG including but not limited to: G Attebury (UNL), M Babik (CERN), M Bly (RAL), N Buraglio (ESnet), T Chown (Jisc), D Christidis (CERN), J Chudoba (FZU Prague), P Demar (FNAL), A Fernandez Casani (IFIC/LHCb), J Flix (PIC), A Forti (GridPP/ATLAS), C Grigoras (CERN/ALICE), B Hoeft (KIT), H Ito (BNL), D P Kelsey (RAL), E Martelli (CERN), S McKee (U Michigan), C Misa Moreira (CERN), R Nandakumar (RAL), K Ohrenberg (DESY), F Prelz (INFN), D Rand (Imperial), A Sciabà (CERN/CMS), Z Shan (IHEP), T Skirvin (FNAL), M Wadenstein (NDGF), C Walker (Jisc) and many others!